## Slide 1: Budget 3D Scanner Project
(Redistribution Edition - Open Source Project)
Hardware & Arduino Programming: Toby
Post-processing & Optimization: Andy

## Slide 2: Introduction
3D Scanners are kind of expensive right now but it has a wide range of application
We want to make a low cost 3D scanner with ToF Sensor and two stepper motors as Proof of Concept
Aim as create somewhat observable 3D models from one single sensor by converting the sensor data into point clouds that construct the 3D model

## Slide 3: Design Sketch
Draft design of the scanner, designed to be completely 3D printable and cheap to build.

## Slide 4: 3D modeling (and render)

## Slide 5: Final Product (Scanner)
Specification:
VL53L1X ToF Sensor (SHARP GP2D12F) Arduino UNO 2.8V Stepper Motor x2 Many 3D Printed Parts

## Slide 6
Top View and Front View

## Slide 7: Scanner In Action

## Slide 8: Raw Output of Scanner

## Slide 9: Processed Scan Data

## Slide 10: Calibration formula deduction

## Slide 11: Assumptions
The placement of calibration box is off centered → unknow center point
The height ratio is straight forward: (top - bottom )/ steps
The depth is the complicated part.
x = depth * sin(theta), y = depth * cos (theta)
But hey the box is off centered and we don’t know any of x and y and theta!

## Slide 12: Derive a function that link everything together
D =
(side /2 + Ox) / sin(theta+offset) | 0<= theta <=pi/2
(side /2 - Oy) / sin(theta+offset) | pi/2<= theta <= pi
(side /2 - Ox) / sin(theta+offset) | pi <= theta <= 3pi/2
(side /2 + Oy) / sin(theta+offset) | 3pi/2<= theta <= 2pi
Too complicate, we can go with only local minimum : (sin(theta)=1)
D
(Ox,Oy)

## Slide 13: Going through the DARKNESS of calculus
We can eliminate variables using differentiation
d D/ dr = 0 ← solve r and left with 1 unknown
can be approximated by D(r+Δr)-D(r)/Δr
Also need to reject d^2 D/ dr > 0 (local max)

## Slide 14: It gots clear at this point
at each local minimum
d_min ± (Ox or Oy) = depth (measured by sensor)
One more trick
let Oy >= Ox
d - Oy <= d - Ox <= d + Ox <= d + Oy
cancel out Oy, done
D
(Ox,Oy)

## Slide 15: Cost Summary
Item Name | Amount / Units | Cost (in HKD) | Remarks
3D Printed Parts | Around 700g | $84 | Estimated Material Cost
VL53L1X | 1 | $336 | Replaced with Infrared sensor due to accident
GP2D12 | 1 | $78 | SHARP Infrared sensor
L298N | 2 | $35.3 x 2 | 
Arduino UNO | 1 | $180.52 | 
M3 * 5, M3 * 10, M3 * 20 screws | >20 | Neglectable | 
 |  | Total (with ToF) | $671.12
 |  | Total (with IR) | $413.12

## Slide 16: Final Results

## Slide 17: Final Results
Transparent parts that cannot be scanned via IR sensor

## Slide 18: Future Development
Use dual sensor mode with Ultrasound Sensor to reduce error from reflection and transparent material
Improve post-processing and scanning accuracy (This ToF Sensor is not the best one to suit this kind of application)
3D Copying Machine! (Scanner directly output gcode for 3D printer to print at the same time)
Open Source

## Slide 19: Thank you

## Slide 20: Reference and CopyRight
All the content in this powerpoint is licensed under IMUS License (Somewhat the same as MIT License with some extra about hardware), All Right Reserved. You can freely distribute this powerpoint with the following restriction
No Commercial Uses
No charge / fees should be involved when distributing this powerpoint and related files inside this project
Toby and Andy (Author of this project) has all right towards this project and all project material. The author will not bear any responsibility to the safety, workability, accuracy or other technical or safety related issue regarding this machine.
Ask for permission for usage if you are using this project (and its material) for any purposes except educational and personal uses purpose.
Visit https://www.facebook.com/ImusLaboratory for more information